## Slide 1: What is a network?
“Combination of hardware, software, and cabling, which together allow multiple computing devices to communicate with each other.”
  “Gives computers the ability to communicate”
  Differences are primarily those of scale
  Often clouds in diagrams
Notes: Quotations from page 5 of Computer Networking First-Step by Wendell Odom (Cisco Press, 2004)
Figures 1-1 and 1-2 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 2: The electrician’s perspective
Cables connecting each wall plate to wiring panels in wiring closets
  Conduit
  Cable runs
Notes: Figure 1-4 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 3: The wiring closet
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 4: The wiring closet
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 5: The wiring closet
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 6: The wiring closet
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 7: The wiring panel
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 8: The wall plate
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 9: The network engineer’s perspective
Patch cables connecting ports on wiring panels to switches
  Each wiring panel port represents a device
  Switches connect those devices to one another as needed
Notes: Figure 1-5 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 10: The switch stack
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 11: The switch stack
Notes: Photo Copyright © 2012 Mike Gildersleeve. All rights reserved.

## Slide 12: The server administrator’s perspective
Network utility
  Cloud
Notes: Figure 1-3 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 13: The user’s perspective
Most don’t need or want to know how it works
  Network utility accessible through wall jack
    Like electricity
  Magic clouds
  Network services
Notes: Figure 2-5 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 14: “Accidental” network usage
User doesn’t even know he’s using the network
  Transparent
    “Sneakernet”
  File access
    File server
  Printing services
    Print server
Notes: Figures 2-1 and 2-5 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 15: “Intentional” network usage
User has some idea the network is required
  Often involves the Internet via an ISP
    Phone or cable modem
  Internet services – client/server model
    E-mail – e-mail client, e-mail server, “snail mail”
    World Wide Web – browser, web server, pages, URLs, sites/presentations
    File Transfer – FTP client, FTP server, upload/download
      Differs from file access
Notes: Figures 2-8 and 2-5 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 16: Types of networks
Local area network – LAN
  Previous figures
  Connects computers that are close together
Wide area network – WAN
  Connects several LANs at different sites
  Enterprise network or enterprise WAN
The Internet
  Connects LANs and WANs all over the world
  Internet Service Provider – ISP
Notes: Figures 1-6 and 1-7 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 17: Networking standards
Sets of rules for creating networking products
  More general than protocols
  Cables, hardware, software
  Interoperability
Physical connectivity
  Devices, NICs, and cabling – path for data
  Connectors – keyed by shape, size, pins, etc.
Notes: Figure 3-1 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 18: A familiar illustration
Electricity is required by many devices
  Viewed as utility
  Standards make things simpler
  Physical configuration standards
  Signaling standards – voltage, amperage, AC/DC
Notes: Figure 3-1 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 19: Common ground for communication
Programs often need to exchange data
  Communication
  File formats
    Text, Word, JPEG, PDF, etc.
    Standard way of representing data as patterns of bits
      Binary digits – 0 and 1
      Bytes – 8 bits
      All files are just collections of bits
Networks’ fundamental job is to move bits around
  Often different voltages are used
    One to represent 0 and another to represent 1
  Sender and receiver must agree as to which is which
  Encoding rules – defined by standards
Notes: Figure 3-1 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 20: Packets
Groups of bits to be sent – like envelopes
  Make transmissions more manageable
  Facilitate error recovery
    Electrical interference
      Crosstalk – one electrical signal influences another
      Can be minimized but not totally eliminated
    Must be some way to identify and replace erroneous packets
    Such facilities are built into networking protocols
      Protocol – standardized process
Notes: Figures 3-2 and 3-3 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 21: Networking models
Aka:
  Networking architectural models
  Networking blueprints
  Network architectures
Collection of standards and protocols designed to be used together
Initially proprietary
  SNA (IBM) vs. DECnet (DEC)
  Gateway required for interoperability
Notes: Figures 3-4 and 3-5 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 22: Public networking models
TCP/IP networking model
  Encompasses several protocols
  Allows all computers to communicate, regardless of manufacturer
  Eventually supplanted proprietary models
  Internet Engineering Task Force (IETF)
    Open to all
    Requests for comment (RFCs)
      www.rfc-editor.org

## Slide 23: Transmission Control Protocol (TCP)
Provides error recovery
  Header added to each segment (packet)
  Contains sequence number
  Also contains number of next packet expected
    Forward acknowledgement
  RFC 793
Notes: Figure 3-6 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 24: Internet Protocol (IP)
Provides logical addressing and routing
  Logical addresses uniquely identify all devices
  Routing moves packets from source to destination
    IP adds its own headers to packets
    Headers contain source address and destination address
    Routers use that info to forward packets based upon their internal routing tables
  Analogous to postal service
  RFC 791
Notes: Figure 3-7 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 25: Some standards bodies
Internet Engineering Task Force (IETF)
  Most of the fundamental Internet standards
  www.ietf.org
Institute of Electrical and Electronic Engineers (IEEE)
  Most standards for physical transmission of bits on LANs
  www.ieee.org
International Telecommunications Union (ITU)
  Most standards for data transmission over WANs using leased lines
  www.itu.int
International Organization for Standardization (ISO)
  OSI Network Model
  www.iso.org
World Wide Web Consortium (W3C or W3)
  Most Web-related standards
  www.w3.org
Many more…

## Slide 26: TCP/IP Network Model
Four or five layer model
  Each encapsulates distinct but essential functionality
  Division of labor with well-defined interfaces
Notes: Figure 3-9 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 27: OSI Network Model
Open Systems Interconnect
  Standardized by ISO
Seven layer model
  Intended to be globally comprehensive
  Almost never actually used in practice
  But terminology is pervasive
    Especially layer names and numbers
Notes: Figure 3-10 from Computer Networking First-Step by Wendell Odom (ISBN: 1587201011) Copyright © 2013 Cisco Systems, Inc. All rights reserved.

## Slide 28: Assignment of Protocols to Layers
Notes: Definition from http://dictionary.reference.com/search?q=communication&x=33&y=25

## Slide 29: Finding your application in TCP/IP
TCP and UDP introduce the concept of ports
Port – how to find “your” application to talk to
Common ports and the services that run on them:
  FTP 21 and 20
  telnet 23
  SMTP 25
  http 80
  POP3 110
  Apache Tomcat (TCP) 8080 - Unofficial
  https://en.wikipedia.org/wiki/List_of_TCP_and_UDP_port_numbers

## Slide 30: Internet Infrastructure

## Slide 31: Internet Infrastructure
The infrastructure of the Internet consists of a federation of connected networks that are each independently managed (“autonomous system”)
  Note: Each “autononmous system may consist of multiple IP networks
An Autonomous System (AS) is a collection of routers whose prefixes and routing policies are under common administrative control.

## Slide 32: Hierarchy of network service providers
Tier-1: nation or worldwide network (US: less than 20)
Tier-2: regional networks (in US: less than 100)
Tier-3: local Internet service provider (in US: several thousand)

## Slide 33: Internet Infrastructure
Hierarchical – Conceptually!

## Slide 34: Tier-1 ISP: e.g., Sprint

## Slide 35: Internet Backbone
Treat each other as equals
Peering – Tier-1 ISPs do not “charge” each other to carry network traffic

## Slide 36: Internet Backbone
“Tier-1” commercial ISPs (e.g., Verizon, Sprint, AT&T, Qwest, Level3), national & international coverage
large content distributors (Google, Akamai, Microsoft)
Tier 1 ISP
Tier 1 ISP
large content
distributor
(e.g., Google)
large content
distributor
(e.g., Akamai)
IXP
IXP
Tier 1 ISP
tier-1 ISPs &
content distributors, interconnect (peer) privately
… or at Internet exchange points IXPs

## Slide 37: IXP (IX)
Internet Exchange Point
  A physical infrastructure through which Internet service providers (ISPs) and Content Delivery Networks (CDNs) exchange Internet traffic between their networks (autonomous systems).

## Slide 38: Terms
PoP
  Point of presence is the point at which two or more different networks or communication devices build a connection with each other. POP mainly refers to an access point, location or facility that connects to and helps other devices establish a connection with the Internet.
  Terminology from “phone” days
  Not to be confused with POP2 or POP3 – Post Office Protocol

## Slide 39: Internet Infrastructure
Location where a network (ISP, corporate network, or regional network) gets access to the Internet at a POP.
Locations (Tier-1 or Tier-2) networks are connected for the purpose of exchanging traffic are called peering points.
  Public peering: Traffic is swapped in a specific location at an IXP
  Private peering: Two networks establish a direct link to each other.

## Slide 40: Internet Infrastructure

## Slide 41: Tier-2
ISPs: smaller (often regional)
  Connect to one or more tier-1 (provider) ISPs
  Each tier-1 has many tier-2 customer nets
  Tier-2 pays tier 1 provider
  Tier-2 nets sometimes peer directly with each other (bypassing tier-1), or at IXP

## Slide 42: Tier 2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
IXP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at IXP

## Slide 43: Tier-3
ISPs, local ISPs
Customer of Tier-1 or Tier 2 Network
  last hop (“access”) network (closest to end systems)

## Slide 44: Tier-3 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
IXP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 45: Internet Infrastructure
Roughly Hierarchical – Conceptually!...
But really a GRAPH!

## Slide 46: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 47: Getting From Here to There…
A packet goes through many networks.
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
IXP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP