## Slide 1: Caching

## Slide 2: How Programs Run
When a program starts, the code is usually on a hard dick or solid state drive
  The OS creates a new process to run the program
  The code is copied to main memory
  The program is started by calling main
Most of the programs data is stored in main memory, but some of the data is stored in registers, small units of memory on the CPU
  Program counter (PC)
    contains the address (in memory) of the next instruction in the program
  Instruction register (IR)
    contains the machine code instruction currently executing
  Stack pointer (SP)
    contains the address of the stack frame for the current function
  General-purpose registers
    hold the data the program is currently working with
  Status register
    contains information about the current computation

## Slide 3: How Programs Run
When a program is running, the CPU executes the following steps called the “Instruction Cycle”
  Fetch
    The next instruction is fetched from memory and stored in the instruction register
  Decode
    Part of the CPU, called the “control unit”, decodes the instruction and sends signals to the other parts of the CPU
  Execute
    Signals from the control unit cause the appropriate computation to occur

## Slide 4: How Programs Run
Computers can execute hundreds of instructions, called “Instruction Set”. Most instructions fall under four categories:
  Load
    Transfers a value from memory to a register
  Arithmetic/logic
    Loads operands from registers, performs a mathematical operation, and stores the result in a register
  Store
    Transfers a value from a register to memory
  Jump/branch
    Changes the program counter, causing the flow of execution to jump to another location in the program

## Slide 5: Cache Performance
A “cache” is a small, fast memory that is physically close to the CPU
current computers typically have several levels of cache
  Level 1 cache, the smallest and fastest, access times near 1 ns (nanosecond)
  Level 2 cache, access times near 4 ns
  Level 3 cache, access times near 16 ns
When the CPU loads a value from memory, it stores a copy in the cache
  If the same value is loaded again, the CPU gets the cached copy and doesn’t have to wait for memory

## Slide 6: Cache Performance
Cache “hit rate” ( h )
  The fraction of memory accesses that find data in cache
Cache “miss rate” ( m )
  The fraction of memory accesses that have to go to memory
If the time to process a cache hit is Th and the time for a cache miss is Tm ,
The average time for each memory access is :
  hTh + mTm

## Slide 7: Locality
The tendency of a program to use the same data more than once is called “temporal locality”
  In a loop, programs execute the same instructions many times
  The result of one instruction is often used immediately as an operand of the next instruction
The tendency to use data in nearby locations is called “spatial locality”
  Most programs contain blocks of code with no jumps or branches. Within these blocks, instructions run sequentially.
  When a program executes a function, its parameters and local variables are stored together on the stack
  One of the most common processing patterns is to read or write the elements of an array sequentially

## Slide 8: Memory Hierarchy
Caches are fast because they are small and close to the CPU, which minimizes delays due to capacitance and signal propagation
  If you make a cache big, it will be slower
Main memory is usually packaged in a dual in-line memory module (DIMM) that includes 16 or more chips
  Several small chips are cheaper than one big one
The trade-off between speed, size, and cost is the fundamental reason for caching

## Slide 9: Memory Hierarchy
Typical access times, sizes, and costs for each of these technologies
Device | Access time | Typical size | Cost
Register | 0.5 ns | 256 B | ?
Cache | 1 ns | 2 MiB | ?
DRAM | 100 ns | 4 GiB | $10 / GiB
SSD | 10 µs | 100 GiB | $1 / GiB
HDD | 5 ms | 500 GiB | $0.25 / GiB
Tape | minutes | 1-2 TiB | $0.02 / GiB
These technologies make up the “memory hierarchy”
  Each level of the hierarchy is bigger and slower than the one above it

## Slide 10: Caching Policy
At every level of the hierarchy, we have to address four fundamental questions of caching:
  Who moves data up and down the hierarchy?
    Top of the hierarchy - register allocation is usually done by the compiler
    Bottom of the hierarchy - administrators move data explicitly between disk and tape.
  What gets moved?
    In general, block sizes are small at the top of the hierarchy and bigger at the bottom
  When does data get moved?
    Data gets moved into cache when it is used for the first time
  Where in the cache does the data go?
    When the cache is full, it kicks data out
    Need to keep data that will be used again soon and replace data that won’t